Ultrafast artificial intelligence at the Edge
Scientific Achievement
Analog signal processing that directly feeds sub-20 microsecond latency machine learned identification of desirable x-ray SASE sub-structure.
Significance and Impact
Analog signal processing logic transforms detector signal to ideal ML-model input.
FPGA-based inference neural network for autonomous decisions with 20 microsecond latency.
Research Details
  1. Initial test with surrogate HHG laser source and newly designed electron Time-of-Flight (ToF) spectrometer
  2. Analog signal processing that transforms raw Micro-channel plate (MCP) signals directly into the representation needed for the neural network.
  3. Shallow neural network for on-the-fly decision making that uses the 16-fold angular array of electron ToF spectrometers
  4. FPGA-based identification of the number of sub-spikes in SASE XFEL shots with decision times below 20 microseconds.
Next Steps
  1. Use 8-fold differential retardation to simulate angular streaking results.
  2. Measure linear streaking in PULSE lab with analog pre-processing circuit and on-digitizer FPGA neural network.
  3. Incorporate recently measured wave forms to benchmark inference fidelity in both over- and under-sampling regimes.
  4. Improve the “confusion matrix” for increasing numbers of SASE sub-spikes.
Non-linear Time-to-analog conversion logic. The top panel shows a few-hit single shot, central demonstrates the non-linear voltage ramp used for the “sample and hold”, and the right panel the resulting histogram.
Work was funded by DOE-BES – Scientific User Facilities under FWP 100498 with personnel support provided by LCLS Experimental Facilities FWP 10074.
[Speaker Notes: HL Type: User___, Staff___, User & Staff___ 1-2 paragraph description of highlight Insert a ~ 200 word description of the highlight here. Collaborating Institutions Funding Overview Section (check all relevant sources) BES Funding: MSED___, CSGB___, EFRC___, SUFD___ SC Funding: ASCR___, BES___, BER___, FES___, HEP___, NP___, WDTS___, SBIR___, etc. Other Funding: DOD___, DOE___, NIH___, NSF___, etc. Funding details for all sources: Publication/ press releases/ related links:]

---
Analog pre-processing for down-stream ML models
Analog signal processing to directly feed sub-20 microsecond latency machine learned identification of desirable x-ray SASE sub-structure.
Identified analog electronics logic for pre-processing of electron Time-of-Flight wave forms that alleviates need for high digitizer bandwidth and sampling.
  1. Initial test using surrogate HHG laser source with prototype electron spectrometer (CookieBox)
  2. Developed analysis chain using analog pre-processing that feeds a non-linear Time-to-Analog converter for transforming raw wave forms directly into the representation needed by the down-stream FPGA-based inference engine.
  3. Next steps: Use known HHG spectra with 8-fold differential retardation to simulate angular streaking results. Install prototype detectors into dual sided streaking geometry in PULSE lab and measure linear streaking with analog pre-processing circuit and on-digitizer logic.
HHG based electron spectra transformed from Time-of-Flight to nearly energy domain using derivative amplifier and software non-linear TAC logic. The top panel shows a few-hit single shot, central demonstrates the non-linear voltage ramp used for the “sample and hold”, and the right panel the resulting histogram.
Work was funded by DOE-BES – Scientific User Facilities under FWP 100498 with personnel support provided by LCLS Experimental Facilities FWP 10074.
[Speaker Notes: HL Type: User___, Staff___, User & Staff___ 1-2 paragraph description of highlight Insert a ~ 200 word description of the highlight here. Collaborating Institutions Funding Overview Section (check all relevant sources) BES Funding: MSED___, CSGB___, EFRC___, SUFD___ SC Funding: ASCR___, BES___, BER___, FES___, HEP___, NP___, WDTS___, SBIR___, etc. Other Funding: DOD___, DOE___, NIH___, NSF___, etc. Funding details for all sources: Publication/ press releases/ related links:]

---
Ultra-low latency inference engine for identifying desirable x-ray shots based on SASE sub-structure
Initial demonstration of ultra-low latency FPGA-based inference for autonomous decisions in data routing and veto; compatible with as few as 20 event buffer depth.
  1. Shallow Neural Network model for Level-0 on-the-fly decision making based on the 16-fold angular array of electron spectrometers (CookieBox)
  2. Correctly identifies single spike versus two spike versus 3 or 4 spike SASE shots with inference latency in the 10 microsecond range for 250MHz clock FPGA.
  3. Next steps: Incorporate recently measured wave forms in both over- and under-sampling regimes. Improve the “purity” of the output confusion matrix for higher number of sub-spikes
SASE sub-structure inference neural network for to infer the fate of streaming data, on the fly, using the CookieBox detector. Neural Network layers by color, 3 layer fully connected neural network, for two representative FPGA clock frequencies.
Work was performed at the LCLS with the help of TID with close integration into L2SI data systems efforts.
[Speaker Notes: HL Type: User___, Staff___, User & Staff___ 1-2 paragraph description of highlight Insert a ~ 200 word description of the highlight here. Collaborating Institutions Funding Overview Section (check all relevant sources) BES Funding: MSED___, CSGB___, EFRC___, SUFD___ SC Funding: ASCR___, BES___, BER___, FES___, HEP___, NP___, WDTS___, SBIR___, etc. Other Funding: DOD___, DOE___, NIH___, NSF___, etc. Funding details for all sources: Publication/ press releases/ related links:]